## Slide 1: Lead-acid Batteries today and tomorrow

## Slide 2
- Both Li-ion and PbA are growing within their
respective markets
WW Battery Market Report Avicenne 2025
- Worldwide battery growth continues

## Slide 3
- Li-ion was developed by Sony for camcorders
- Unanticipated Consequences
New products
New markets
Massive Growth in Li-ion sales
Nobel Prize for the Li-ion inventors!

## Slide 4
But the growth in the Li-ion market resulted from the creation of new products for new markets that were not possible without Li-ion, such as those shown at the right.
These are not (and were not) PbA markets
Therefore, PbA is mostly unaffected from this Li-ion growth but… the overcapacity of the Li-ion industry is now beginning to impact PbA especially where cycle life is an issue.

## Slide 5
Global Lead Battery Market

## Slide 6
Multiple Sources Report
That “Lead is definitely NOT Dead!”
CARGs Reported 2-5% til 2034
Grand View Horizon
GRMU Insights.org

## Slide 7
And expected to grow in the Emerging Market of
“Battery Energy Storage Systems” (BESS or ESS)
PbA - Still Growing in existing markets
Lead Battery Market Data - CBI 2025

## Slide 8
Other
Emerging Battery Technologies

## Slide 9
Emerging Battery Technologies
Advanced Li-ion
Na-ion
Solid State
Flow Batteries
Zinc Batteries

## Slide 10
Advanced Li-ion Batteries
Players – CATL, BYD and many others.
Markets – EV’s, Energy Storage, Consumer electronics
Safety improvements and the elimination of cobalt are driving these advances. These improvements are being done to hedge against new Sodium-ion battery developments in the EV and ESS markets.

## Slide 11
Sodium-ion Batteries
Players – CATL, BYD, Natron Energy, Faradion, Altris
Markets – Energy Storage, Renewable Energy, Low Speed EV’s. Telecom, Consumer electronics. Taking market share from Li-ion.
Sodium-ion (Na-ion) batteries are being developed as a lower cost option to Li-ion and offer a solution to raw material (Lithium) availability in the EV and ESS markets.

## Slide 12
Solid State (Li-ion) Batteries
Players – Toyota, Quantum Scape, Solid Power, Samsung SDI, Mercedes
Markets – EV’s, Aviation, Drones, Consumer electronics, Energy Storage
Potential Safety Improvements (aka fires) are driving solid-state battery development for the EV market. There is no significant production yet, and only pilot line prototypes are available for testing at this time.

## Slide 13
Redox Flow Batteries
Players – Invinity, Sumitomo, Stryten, VRB Energy, RedFlow, CellCube
Markets – Long Duration Energy Storage,
Vanadium Flow batteries are seen as a good fit for the Long Duration Energy Storage (LDES) and Microgrid markets. Capacity can be increased by simply adding larger electrolyte tanks.

## Slide 14
Zinc Batteries – Zn-Air and Ni-Zn
Players – Zinc 8, ZAF Energy, EnZinc, Zinc5, NantEnergy, Phinergy
Markets – Long duration ESS,
Zn-Air has 2X the energy density of Li-ion, but rechargeability tends to be a problem. Systems are being prototyped in the LDES market. Several recent fires at Zinc5 sites are problematic.

## Slide 15
The Issues for Pb

## Slide 16
Pb Cycle Life
At the present time
Li-ion ~4X better cycle life than PbA.
Major improvement in PbA cycle life is needed!
Though not actual data, this chart from the DOE does present a realistic comparison between state-of-the-art Li-ion and PbA

## Slide 17
LCOS
Levelized Cost of (energy) Storage
LCOS for 10 Hr Discharge shown >>>>
Li-ion LFP= $0.18 $/KWh
Li-ion NMC = $0.24 $/KWh
PbA = $0.29 $/KWh
DOE Target = $0.05 $/KWh
With major improvements in cycle life PbA LCOS should reach <$0.10/KWh

## Slide 18
All the PbA issues
- Cycle life & LCOS
- Dynamic Charge Acceptance (DCA)
- Specific Energy (Wh/Kg)
- Huge manufacturing base resistant to change
- Emerging battery technologies

## Slide 19
How to address the Issues
- Bipolar offers:
Improved cycle life
Reduced Lead Content
Reduced Cost
Higher Specific Energy
Improved Pulse Power
- Carbon additives in the NAM improve DCA
- Carbon fiber negatives reduce cost & weight
- Conductive fillers in the PAM improve cycle life
- More innovation required!

## Slide 20
Conclusions
- Increased Pb cycle life will expand deep cycle
market options (ESS, Off-Grid, Golf Car & others)
- Pb safety (not flammable like Li-ion) will facilitate
penetration into residential solar ESS markets
- Meeting DOE LCOS targets will lead to more
government funding
- Specific energy not an issue for non-portable
market segments
- Emerging tech will directly threaten Li-ion markets and
not PbA markets

## Slide 21
Terra Supreme Battery has the solution!
-

## Slide 22
TSB G-31 Advantages
- Bipolar / VRLA
- Horizontal plate format
eliminates acid stratification
- Reduced Pb content
- 3X cycle life of
conventional PbA/VRLA
- High Specific Energy
- Max Pulse Power
- Fully recyclable

## Slide 23
TSB G31 Target Markets

## Slide 24
TSB G31
Competition, Markets &
Benefits
Most TSB G31 Markets are not threatened by emerging tech!

## Slide 25
US Battery
Competition

## Slide 26
US Battery Manufacturers
Lead-Acid
Clarios
EnerSys
Stryten
Crown Battery
C&D Technologies
Advanced Battery Concepts
Gridtential
Li-ion
Tesla / Panasonic
LG Energy Solutions
SK On
GM and Ultium

## Slide 27
For questions contact –
George H. Brilmyer, Ph.D.
Batt-Tek Consulting
(423) 202-8467
https://batt-tekconsulting.com/